## Slide 1: Introduction to VAV Diffusers

## Slide 2: Copyright Materials
This presentation is protected by U.S. and international copyright laws. Reproduction, distribution, display and use of this presentation without written permission of the speaker is prohibited.
® Price Industries, Incorporated 2023

## Slide 3: VAV Diffusers
Introduction to VAV diffusers, how they work, and how to use them in HVAC system designs.
Course Description

## Slide 4: VAV Diffusers
By the end of this lecture, you will be able to:
  Describe what a VAV diffuser is and how it works
  Identify design features unique to VAV diffusers
  Outline basic system design principles
Learning Objectives

## Slide 5: Overview
Comfort
How VAV Diffuser Work
Benefits
Design Basics
Example Projects
Product Summary
Agenda

## Slide 6: Comfort

## Slide 7: VAV Diffusers
A ceiling diffuser with an individual thermostat and built-in VAV damper.
What are VAV Diffusers?

## Slide 8: VAV Diffusers
Like having a little VAV box in each space.
What are VAV Diffusers?

## Slide 9: VAV Diffusers
Like having a little VAV box in each space.

## Slide 10: VAV Diffusers
Like having a little VAV box in each space.
What are VAV Diffusers?

## Slide 11: VAV Diffusers
Like having a little VAV box in each space.
What are VAV Diffusers?

## Slide 12: VAV Diffusers
Like having a little VAV box in each space.
What are VAV Diffusers?

## Slide 13: VAV Diffusers
Like having a little VAV box in each space.
What are VAV Diffusers?

## Slide 14: VAV Diffusers
Like having a little VAV box in each space.
What are VAV Diffusers?
T
T
T
T
T

## Slide 15: VAV Diffusers
This allows for individual comfort.
What are VAV Diffusers?
T
T
T
T
T

## Slide 16: VAV Diffusers
Each VAV diffuser location provides an opportunity for customized adjustment.
What are VAV Diffusers?
74°
T
72°
T
73°
T
70°
T
76°
T

## Slide 17: VAV Diffusers
Adjusting each individual space to the inevitable load changes.
What are VAV Diffusers?
74°
T
72°
T
73°
T
70°
T
76°
T

## Slide 18: VAV Diffusers
Using fewer resources – no over cooling or over heating of individual spaces.
What are VAV Diffusers?
74°
T
72°
T
73°
T
70°
T
76°
T

## Slide 19: VAV Diffusers
A diffuser with the VAV damper and thermostat built in.
What are VAV Diffusers?

## Slide 20: VAV Diffusers
A diffuser with the VAV damper and thermostat built in.
What are VAV Diffusers?
Individual control

## Slide 21: VAV Diffusers
Air Distribution
What are VAV Diffusers?

## Slide 22: VAV Diffusers
Air Distribution
The Coanda effect (or wall-attachment effect) is the tendency of a moving fluid, either liquid or gas, to attach itself to a surface and flow along it - Henri Coanda 1930
What are VAV Diffusers?

## Slide 23: VAV Diffusers
Air Distribution
What are VAV Diffusers?

## Slide 24: VAV Diffusers
Air Distribution
What are VAV Diffusers?

## Slide 25: VAV Diffusers
Air Distribution
What are VAV Diffusers?

## Slide 26: VAV Diffusers
Air Distribution
What are VAV Diffusers?

## Slide 27: VAV Diffusers
What are VAV Diffusers?
Select equipment for design conditions.

## Slide 28: VAV Diffusers
What are VAV Diffusers?
VAV Systems operate at or below 50% turndown for 85% of the time!
Select equipment for design conditions.

## Slide 29: VAV Diffusers
Variable opening – high discharge velocity – good room air movement at design and turndown conditions
What are VAV Diffusers?
VAV Systems operate at or below 50% turndown for 85% of the time!
Select equipment for design conditions.

## Slide 30: VAV Diffusers
Modeling - CFD Analysis: Airflow pattern colored by temperature - Isometric View
Computational Fluid Dynamics Software
ANSYS - CFX-5 Solver Theory and Solver Modeling
What are VAV Diffusers?
100% Air Flow 25% Air Flow

## Slide 31: VAV Diffusers
Variable opening – high discharge velocity – good room air movement at design and turndown conditions
What are VAV Diffusers?
100% Air Flow 50% Air Flow 25% Air Flow
No Dumping
VAV Diffuser
VAV Diffuser
VAV Diffuser
Poor Diffuser Dumping

## Slide 32: VAV Diffusers
Variable opening = constant discharge velocity
Maintains room air distribution:
Coanda (no dumping)
Throw
Entrainment
Mixing
Under design and turndown conditions
What are VAV Diffusers?

## Slide 33: VAV Diffusers
A diffuser with the VAV damper and thermostat built in.
What are VAV Diffusers?
Individual control

## Slide 34: VAV Diffusers
A diffuser with the VAV damper and thermostat built in.
What are VAV Diffusers?
Individual control
Superior air distribution

## Slide 35: VAV Diffusers
A diffuser with the VAV damper and thermostat built in.
What are VAV Diffusers?
Individual control
Superior air distribution
Comfort!

## Slide 36: Benefits

## Slide 37: VAV Diffusers
Comfort
  Individual Zones of Control – built in thermostat
  Room Air Mixing – built in VAV damper
Benefits

## Slide 38: VAV Diffusers
Comfort
Reliability
  No maintenance
  Varitherm - 10 Year Warranty
  Prodigy - 1 year Warranty
Benefits

## Slide 39: VAV Diffusers
Comfort
Reliability
Adaptable Design
  Walls may be relocated without splitting zone
Benefits

## Slide 40: VAV Diffusers
Comfort
Reliability
Adaptable Design
Energy Efficiency
  Low pressure system
  Small zones of control
Benefits

## Slide 41: VAV Diffusers
Compare installed costs of the system
Size of Zone Cost vs. Comfort
Cost
$
$$
$$$

## Slide 42: VAV Diffusers
Compare installed costs of the system
Size of Zone Cost vs. Comfort
Cost
$
$$
$$$
$$
VAV Diffusers

## Slide 43: How VAV Diffuser Work

## Slide 44: VAV Diffusers
Mechanical (thermal) Varitherm (VPD)
Digital (electric) Prodigy (PPD)
How VAV Diffusers Work
VPD
PPD

## Slide 45: VAV Diffusers
Varitherm (VPD)
Thermostat Actuator
Accurate
Repeatable
Reliable
Robust
How VAV Diffusers Work

## Slide 46: VAV Diffusers
Varitherm (VPD)
How VAV Diffusers Work

## Slide 47: VAV Diffusers
Varitherm (VPD)
How VAV Diffusers Work

## Slide 48: VAV Diffusers
Varitherm (VPD)
How VAV Diffusers Work

## Slide 49: VAV Diffusers
Varitherm (VPD)
How VAV Diffusers Work

## Slide 50: VAV Diffusers
varitherm (VPD)
How VAV Diffusers Work

## Slide 51: VAV Diffusers
Varitherm (VPD)
How VAV Diffusers Work

## Slide 52: VAV Diffusers
Prodigy (PPD)
How VAV Diffusers Work

## Slide 53: VAV Diffusers
Prodigy (PPD)
How VAV Diffusers Work

## Slide 54: VAV Diffusers
Prodigy (PPD)
How VAV Diffusers Work

## Slide 55: VAV Diffusers
Prodigy
How VAV Diffusers Work
or
Master and up to 5 Drones
Standalone

## Slide 56: VAV Diffusers
Prodigy
How VAV Diffusers Work
BACnet Network

## Slide 57: VAV Diffusers
Prodigy
How VAV Diffusers Work
PPD
PSD
PRD
PLD

## Slide 58: Design Basics

## Slide 59: VAV Diffusers
Small Zones of Control
One or two Small Rooms
Design Basics
Application and Design

## Slide 60: VAV Diffusers
Small Zones of Control
Group of Small Spaces
Design Basics

## Slide 61: VAV Diffusers
Small Zones of Control
Complete Building
Design Basics

## Slide 62: VAV Diffusers
Sizing and Locating
Zoning
Pressure Control
Supply Air Temperature
Design Basics

## Slide 63: VAV Diffusers
Sizing and Locating
Size and locate VAV diffusers
as you would ANY diffuser
Design Basics

## Slide 64: VAV Diffusers
Sizing and Locating - Varitherm
At least 2ft/0.6m from obstruction not to disturb room air induction and entrainment
OK Near dropped light Near wall – use
or beam – use directional baffle
directional baffle
Design Basics

## Slide 65: VAV Diffusers
Sizing and Locating
VAV Cooling Only – heights around 20ft/6m
VAV Heating – below 10ft/3m preferred
Design Basics

## Slide 66: VAV Diffusers
Sizing and Locating
Max Flow - Balancing
Manual volume damper at takeoff to diffuser
Open diffuser for balancing
Minimum Flow - Ventilation
Set at diffuser
Design Basics

## Slide 67: VAV Diffusers
Sizing and Locating
Zoning
Design Basics

## Slide 68: VAV Diffusers
Zoning – Heating and Cooling
Provide correct building zoning
(e.g. separating North Perimeter from Interior and from South Perimeter)
Multiple AHU/RTU
Separate Perimeter System
Reheat System
Design Basics

## Slide 69: VAV Diffusers
Zoning – Heating and Cooling
Create larger zones of like usage and exposure and sub zone with VAV diffusers
Design Basics

## Slide 70: VAV Diffusers
Sizing and Locating
Zoning
Pressure Control
Design Basics

## Slide 71: VAV Diffusers
Pressure Control
Objectives:
Provide high enough static pressure
  0.05”wg / 12Pa minimum
Limit the static pressure
  0.25”wg / 62Pa max to limit noise
Pressure independence
Design Basics

## Slide 72: VAV Diffusers
Pressure Control
Methods:
Fan speed control
Design Basics

## Slide 73: VAV Diffusers
Pressure Control
Methods:
Zone control plus
Fan speed control
Design Basics

## Slide 74: VAV Diffusers
Pressure Control
Methods:
Zone control plus
Fan speed control
Design Basics
Pressure Control
Valve (PCV)

## Slide 75: VAV Diffusers
Pressure Control
Methods:
Bypass
(Constant volume fan)
Design Basics
Pressure Control
Valve (PCV)

## Slide 76: VAV Diffusers
Pressure Control
Methods:
Diffuser Bypass
(Constant volume fan)
Requires plenum return
Design Basics
Pressure Relief Collar (PRC)

## Slide 77: VAV Diffusers
Sizing and Locating
Zoning
Pressure Control
Supply Air Temperature
Design Basics

## Slide 78: VAV Diffusers
Supply Air Temperature
Objectives:
Provide consistent supply air temperature
  Can reset supply air temperature
Limit the supply air temperature - Varitherm
  Cooling 50˚F/10˚C to 68˚F/20˚C
  Heating 80˚F/26.5˚C to as low as possible but not to exceed120˚F/49˚C
Provide changeover from cooling to heating
Design Basics

## Slide 79: VAV Diffusers
Supply Air Temperature
Methods:
Consistent SAT
Limit SAT
Design Basics

## Slide 80: VAV Diffusers
Supply Air Temperature
Methods:
Changeover
Design Basics

## Slide 81: Example Projects

## Slide 82: VAV Diffusers
One or two small rooms part of a larger space
Pressure control
<30% by volume
VAV Diffuser
(VPD or PPD)
Example Projects
2022-0208-01 CA Oakmead

## Slide 83: VAV Diffusers
Sub-zone similar spaces
Reheat System
Pressure control and Heat (PCV or SDV)
VAV Diffuser
(VPD or PPD)
Example Projects

## Slide 84: VAV Diffusers
Sub-zone similar spaces
Reheat System
Pressure control and Heat (PCV or SDV)
VAV Diffuser
(VPD or PPD)
Example Projects
2022-0208-01 CA Oakmead

## Slide 85: VAV Diffusers
Example Projects
Unit dedicated to multiple small zones
RTU, HP, FCU, FPB, etc…
Fan speed
VAV Diffuser

## Slide 86: VAV Diffusers
Zoning by dedicated unit RTU/AHU
Pressure control and Heat (PCV or SDV)
VAV Diffuser
(VPD or PPD)
Example Projects

## Slide 87: VAV Diffusers
Sub-zone sections of a building
Separate perimeter system
VAV Diffuser
(VPD or PPD)
Active Chilled
Beam (ACBL)
Example Projects
PG&E

## Slide 88: VAV Diffusers
Sub-zone whole
building
Reheat system
VAV Diffuser
Digital PPD
VAV Diffuser
Mechanical VPD
Example Projects
Kaiser 1600 Owens

## Slide 89: Product Summary

## Slide 90: VAV Diffusers
Product Summary
VPD
Prodigy Series
PRC PCV
PPM
PRTU
PRTU-WEB

## Slide 91: VAV Diffusers
Benefits
Summary

## Slide 92: VAV Diffusers
Benefits
  Comfort
Summary

## Slide 93: VAV Diffusers
Benefits
  Comfort
    Individual Zones
    Good room air mixing
Summary

## Slide 94: VAV Diffusers
Benefits
  Comfort
    Individual Zones
    Good room air mixing
  Reliability
Summary

## Slide 95: VAV Diffusers
Benefits
  Comfort
    Individual Zones
    Good room air mixing
  Reliability
  Adaptable Design
Summary

## Slide 96: VAV Diffusers
Benefits
  Comfort
    Individual Zones
    Good room air mixing
  Reliability
  Adaptable Design
  Energy Efficient Design
Summary

## Slide 97: VAV Diffusers
System Design
Summary

## Slide 98: VAV Diffusers
System Design
Pressure Control
Summary

## Slide 99: VAV Diffusers
System Design
Pressure Control
Supply Air Temperature Control
Summary

## Slide 100: VAV Diffusers
System Design
Pressure Control
Supply Air Temperature Control
Zoning
Summary

## Slide 101: Questions?